AirPro 24-port GbE Switch + 4 Combo GbE Ports with 24 PoE ports

###### Product Specification

Version 1.10

# General Description

Support 24*RJ45 ports + 4*RJ45/SFP combo ports

Support 24 PoE ports, follow IEEE802.3at and IEEE802.3af

# System Specifications

## Hardware spec

| Items | Specifications |
| --- | --- |
| Key Components | RTL8382M+RTL8218Bx2+RTL8214FC PD69200+PD69208x3 |
| I/O ports | 24x GbE ports, RJ45 4x GbE combo ports, RJ45 + SFP |
| PoE ports | Port# 1~ 24 IEEE802.3at, IEEE802.3af PoE power budget: 400W |
| LED Define | SYS: Green LED Off: power off or fail On: power on Blinking: system booting up PoE Max. :Green LED Off: No over PoE max power budget On: Over PoE max power budget 24 RJ45 Port LED: one bi-color LEDs on daughter board Link/ACT: Green/Amber Off: port disconnected or link fail Green on: 1000Mbps connected Amber on: 10/100Mbps connected Blinking: sending or receiving data PoE: Green LED Off: PoE power output off Green on: PoE power output on Blinking: PoE power output over >30W (No Powering) 4 Combo port LED: RJ45: one bi-color LEDs on daughter board - Off: disconnected or fail - Green: 1000Mbps connected - Amber: 10/100Mbps connected - Blinking: data transmitting SFP: one LEDs on daughter board - Off: disconnected or fail - Green: 1000Mbps connected - Blinking: data transmitting |
| HW feature | IEEE802.3 10BASE-T IEEE802.3u 100BASE-TX IEEE802.3ab 1000BASE-T IEEE802.3az EEE IEEE802.3at, IEEE802.3af Switch Capacity: 52Gbps bi-direction Forwarding Mode: Store and Forward MAC address Table: 8K Packet buffer size: 1M bit Jumbo Frame: 9K bytes |
| Power Input | Internal power supply Input: 100-240V AC Output: 450W E-cap life time >3 years @ 40℃ |
| PoE Output power capacity |  |
| PoE Power Budget | Supported 450W power supply 400W power Budget |
| Reset button | Support reset to default config |
| Dimension | 441mmx270mmx45mm |
| FAN Design | Fan*2 with Fan tray |
| Temperature | Operating: 0 ~ 40℃ Storage : -40 ~ 70℃ |
| Humidity | Operating: 10% ~ 90% RH (non-condensing) Storage : 5% ~ 90% RH (non-condensing) |

## Feature

| Model | Model | WEB Smart |
| --- | --- | --- |
| Network | DHCP Client | Yes |
|  | DHCPV6 Client | Yes |
|  | SNTP | Yes |
| Link Aggregation | LACP Link groups | 8 |
|  | LACP Load balance | Yes |
|  | Static Trunk | 8 |
| Port | Port Configuration |  |
|  | EEE | Yes |
|  | Jumbo Frame | Yes |
| VLAN | IEEE802.1Q VLAN | Yes |
|  | VLAN Groups | 256 |
|  | Voice VLAN | Yes |
|  | Protocol VLAN | No |
|  | MAC VLAN | No |
|  | Surveillance VLAN | Yes |
| Spanning Tree | 802.1d (STP) | Yes |
|  | 802.1w (RSTP) | Yes |
|  | 802.1s (MSTP) | No |
| LLDP | LLDP | Yes |
|  | LLDP-MED | Yes |
| Multicast | IGMP Snooping v1/v2/v3 | Yes(No V3) |
|  | IGMP Snooping Queries | Yes |
|  | Block unknown multicast trafic | Yes |
|  | Multicast groups | 256 |
|  | MLD Snooping v1/v2 | Yes |
|  | Multicast VLAN registration (MVR) | No |
| Authentication | RADIUS | Yes |
|  | TACACS+ | Yes |
|  | Management VLAN | No |
|  | Management ACL | No |
|  | 802.1x | Yes |
|  | MAC-Based | No |
|  | WEB-Based | No |
|  | Guest VLAN | No |
| Security | Port Security | Yes |
|  | Storm Control | Yes |
|  | DoS | Yes |
|  | Dynamic ARP Inspection | Yes |
|  | DHCP Snooping | Yes |
|  | IP Source Guard | Yes |
| ACL | MAC ACL | Yes |
|  | IPV4 ACL | Yes |
|  | IPV6 ACL | Yes |
| QoS | Port-based QoS | No |
|  | IEEE802.1p QoS | Yes |
|  | IP Precedence based CoS | Yes |
|  | DSCP based CoS | Yes |
|  | Priority Queues | 8 |
|  | Scheduling Algorithm | SP+WRR |
| Rate Limiting | Ingress rate limiting | Yes |
|  | Egress rate limiting | Yes |
| Mirror | Port Mirroring on ingress and egress | Yes |
|  | Many to One | Yes |
| Log | System Log | Yes |
|  | Logging Server | No |
| Diagnostics | Ping | No |
|  | Traceroute | No |
|  | Cable Test | No |
|  | Fiber Module Information | No |
|  | UDLD | No |
| Management | User Account | Yes |
|  | WEB UI | Yes |
|  | CLI | No |
|  | Telnet | Yes |
|  | Firmware upgrade by WEB UI | Yes |
|  | Firmware upgrade by TFTP | Yes |
|  | Dual Image | No |
|  | config upload/download by WEB UI | Yes |
|  | SNMP V1/V2/V3 | Yes |
|  | SNMP Trap | Yes |
|  | RMON | Yes |
| Loop Detection/Prevention | Loop detection | No |
|  | Loop prevention | Yes |

## Mechanical Drawings

## Front Panel

3.1   EMI/Safety

| Item | Description | Remark |
| --- | --- | --- |
| Safety | CE, LVD | EN 60950-1 |
| EMC | FCC Part15 |  |
|  | CE (Class A) |  |