AirPro 8-port GbE Switch + 4 Combo GbE Ports w/ 8 PoE+ ports

###### Product Specification

Version 1.00

# General Description

Support 8*RJ45 ports + 4*RJ45/SFP ports

Support 8 PoE ports, follow IEEE802.3at and IEEE802.3af

Support Web UI for configuration

# System Specifications

## Hardware spec

| Items | Specifications |
| --- | --- |
| Key Components | RTL8382M+RTL8214FC IC+ IP808 PSE controller |
| I/O ports | 8x GbE ports, RJ45 4 x GbE combo ports, RJ45 + SFP Reset Button: reset to default setting, re-start system |
| PoE ports | Port# 1~ 8 IEEE802.3at, IEEE802.3af PoE power budget: 130W Power supply |
| LED Define | SYS: Green LED Off: power off or fail On: power on Blinking: system booting up PoE Alert: Green LED Off: No over PoE Max power budget (120W) On: Over PoE Max power budget (120W) Port LED: Link/ACT: Off: port disconnected or link fail Green on: 1000Mbps connected Amber on: 10/100Mbps connected Blinking: sending or receiving data PoE: Off: PoE power output off Green on: PoE power output on 4 Combo port LED: RJ45: - Off: disconnected or fail - Green: 1000Mbps connected - Amber: 10/100Mbps connected - Blinking: data transmitting SFP: - Off: disconnected or fail - Green: 1000Mbps connected - Amber: 100Mbps connected - Blinking: data transmitting |
| HW feature | IEEE802.3 10BASE-T IEEE802.3u 100BASE-TX IEEE802.3ab 1000BASE-T IEEE802.3az EEE IEEE802.3at, IEEE802.3af MAC address Table: 8K Packet buffer size: 4.1M Jumbo Frame: 9K bytes |
| PoE power pin-out | Alternative A (Pin 1,2/3,6) |
| PoE Output power capacity | Maximum output :30W per each port Compliant with IEEE802.3af/at standard, Following IEEE802.3at/at to support PoE or PoE+ Automatically discover the connection of PD device and immediately sends power to it Auto disable port if the port current is over 700mA or short happens Priority default setting is lower port NO. has high priority The maximum power used by power devices is defined by the following classification. When Port works in Auto Mode, the output port power limit will be associated with PD classification Value. Follow the standard PSE pin-out standard of Alternative A (MAD-X) which is sending out power over number 1,2,3,6 pins of 8 wires of Ethernet CAT5 UTP cable |
| Power Input | Internal power supply Input: 100-240V AC Output: 160W |
| PoE Power Budget | 130W |
| Reset button | Support reset to default config |
| Dimension | 265(W) x 183(D) x 44(H) mm |
| FAN Design | Fan-less |
| Temperature | Operating: 0 ~ 40℃ Storage : -40 ~ 70℃ |
| Humidity | Operating: 10% ~ 90% RH (non-condensing) Storage : 5% ~ 90% RH (non-condensing) |

| Model | Model | WEB Smart |
| --- | --- | --- |
| Network | DHCP Client | Yes |
|  | DHCPV6 Client | Yes |
|  | SNTP | Yes |
| Link Aggregation | LACP Link groups | 8 |
|  | LACP Load balance | Yes |
|  | Static Trunk | 8 |
| Port | Port Configuration |  |
|  | EEE | Yes |
|  | Jumbo Frame | Yes |
| VLAN | IEEE802.1Q VLAN | Yes |
|  | VLAN Groups | 256 |
|  | Voice VLAN | Yes |
|  | Protocol VLAN | No |
|  | MAC VLAN | No |
|  | Surveillance VLAN | Yes |
| Spanning Tree | 802.1d (STP) | Yes |
|  | 802.1w (RSTP) | Yes |
|  | 802.1s (MSTP) | No |
| LLDP | LLDP | Yes |
|  | LLDP-MED | Yes |
| Multicast | IGMP Snooping v1/v2/v3 | Yes(No V3) |
|  | IGMP Snooping Queries | Yes |
|  | Block unknown multicast trafic | Yes |
|  | Multicast groups | 256 |
|  | MLD Snooping v1/v2 | Yes |
|  | Multicast VLAN registration (MVR) | No |
| Authentication | RADIUS | Yes |
|  | TACACS+ | Yes |
|  | Management VLAN | No |
|  | Management ACL | No |
|  | 802.1x | Yes |
|  | MAC-Based | No |
|  | WEB-Based | No |
|  | Guest VLAN | No |
| Security | Port Security | Yes |
|  | Storm Control | Yes |
|  | DoS | Yes |
|  | Dynamic ARP Inspection | Yes |
|  | DHCP Snooping | Yes |
|  | IP Source Guard | Yes |
| ACL | MAC ACL | Yes |
|  | IPV4 ACL | Yes |
|  | IPV6 ACL | Yes |
| QoS | Port-based QoS | No |
|  | IEEE802.1p QoS | Yes |
|  | IP Precedence based CoS | Yes |
|  | DSCP based CoS | Yes |
|  | Priority Queues | 8 |
|  | Scheduling Algorithm | SP+WRR |
| Rate Limiting | Ingress rate limiting | Yes |
|  | Egress rate limiting | Yes |
| Mirror | Port Mirroring on ingress and egress | Yes |
|  | Many to One | Yes |
| Log | System Log | Yes |
|  | Logging Server | No |
| Diagnostics | Ping | No |
|  | Traceroute | No |
|  | Cable Test | No |
|  | Fiber Module Information | No |
|  | UDLD | No |
| Management | User Account | Yes |
|  | WEB UI | Yes |
|  | CLI | No |
|  | Telnet | Yes |
|  | Firmware upgrade by WEB UI | Yes |
|  | Firmware upgrade by TFTP | Yes |
|  | Dual Image | No |
|  | config upload/download by WEB UI | Yes |
|  | SNMP V1/V2/V3 | Yes |
|  | SNMP Trap | Yes |
|  | RMON | Yes |
| Loop Detection/Prevention | Loop detection | No |
|  | Loop prevention | Yes |

## Mechanical Drawings

## Front Panel

4.1   EMI/Safety

| Item | Description | Remark |
| --- | --- | --- |
| Safety | CE, LVD | EN 60950-1 |
| EMC | FCC Part15 |  |
|  | CE (Class A) |  |