AirPro –AP-EGS4128

24-port GbE Managment Switch + 4 GbE Uplink Port Switch

###### Product Specification

Version 1.00

Revision History

| Date | Release | Author | Description |
| --- | --- | --- | --- |
| 2016/10/28 | 1.00 | Benson Kuo | Draft Release |

# General Description

Support 24*RJ45 ports + 4*RJ45/SFP combo ports

Support Web UI for configuration

Support Console port with CLI command

# System Specifications

## Hardware spec

| Items | Specifications |
| --- | --- |
| Model No. | AP-EGS4128 |
| Key Components | RTL8382M+RTL8218Bx2+RTL8214FC Flash IC: MXIC 16M Byte |
| I/O ports | 24x GbE ports, RJ45 4 x GbE combo ports, RJ45 + SFP Reset Button: reset to default setting, re-start system RJ45 Console port |
| LED Define | PWR: Green LED Off: power off or fail On: power on SYS: Green LED Off: power off or fail On: system is ready Blinking: system booting up Alert: Red LED (option) Off: Switch is normal condition On: Alarm for system failure because of overheat, wrong voltage. Port LED: Link/ACT: Off: port disconnected or link fail Green on: 1000Mbps connected Amber on: 10/100Mbps connected Blinking: sending or receiving data 4 Combo port LED: RJ45: - Off: disconnected or fail - Green: 1000Mbps connected - Amber: 10/100Mbps connected - Blinking: data transmitting SFP: - Off: disconnected or fail - Green: 1000Mbps connected - Amber: 100Mbps connected - Blinking: data transmitting |
| HW feature | IEEE802.3 10BASE-T IEEE802.3u 100BASE-TX IEEE802.3ab 1000BASE-T IEEE802.3az EEE IEEE802.3at, IEEE802.3af MAC address Table: 8K Packet buffer size: 4.1M Jumbo Frame: 9K bytes |
| Dying Gasp | System support Dying Gasp for HW detection. Default set voltage is 10.6VDC. HW can be flexible tuning Dying Gasp Voltage. |
| System Monitor (Option) | HW Monitor IC: ADT7463 Voltage Monitor Input Voltage : 12V (+/-7% Alarm Threshold) I/O Voltage : 3.3V (+/- 5% Alarm Threshold) DDR Voltage : 1.5V (+/- 5% Alarm Threshold) PHY Voltage : 1.1V (+/- 5% Alarm Threshold) MAC Voltage:1.0V (+/- 5% Alarm Threshold) Temperature Monitor BOARD: 0~80C MAC: 0~85C PHY: 0~85C |
| Power Input | Internal power supply Input: 90~264VAC/47~63Hz Output: 12V/3A |
| Reset button | Support reset to default configuration |
| Dimension | 441(W) x 196(D) x 44(H) mm |
| FAN Design | Fan-less |
| Temperature | Operating: 0 ~ 50℃ Storage : -40 ~ 70℃ |
| Humidity | Operating: 10% ~ 90% RH (non-condensing) Storage : 5% ~ 90% RH (non-condensing) |

## 2.2    Software Spec

| Model | Model | WEB Smart | L2 Switch |
| --- | --- | --- | --- |
| Network | DHCP Client | Yes | Yes |
|  | DHCPV6 Client | Yes | Yes |
|  | SNTP | Yes | Yes |
| Link Aggregation | LACP Link groups | 8 | 8 |
|  | LACP Load balance | Yes | Yes |
|  | Static Trunk | 8 | 8 |
| Port | Port Configuration | Yes | Yes |
|  | EEE | Yes | Yes |
|  | Jumbo Frame | Yes | Yes |
| VLAN | IEEE802.1Q VLAN | Yes | Yes |
|  | VLAN Groups | 256 | 256 |
|  | Voice VLAN | Yes | Yes |
|  | Protocol VLAN | No | Yes |
|  | MAC VLAN | No | Yes |
|  | Surveillance VLAN | Yes | Yes |
| Spanning Tree | 802.1d (STP) | Yes | Yes |
|  | 802.1w (RSTP) | Yes | Yes |
|  | 802.1s (MSTP) | No | Yes |
| LLDP | LLDP | Yes | Yes |
|  | LLDP-MED | Yes | Yes |
| Multicast | IGMP Snooping v1/v2/v3 | Yes(No V3) | Yes |
|  | IGMP Snooping Queries | Yes | Yes |
|  | Block unknown multicast trafic | Yes | Yes |
|  | Multicast groups | 256 | 256 |
|  | MLD Snooping v1/v2 | Yes | Yes |
|  | Multicast VLAN registration (MVR) | No | Yes |
| Authentication | RADIUS | Yes | Yes |
|  | TACACS+ | Yes | Yes |
|  | Management VLAN | No | Yes |
|  | Management ACL | No | Yes |
|  | 802.1x | Yes | Yes |
|  | MAC-Based | No | Yes |
|  | WEB-Based | No | Yes |
|  | Guest VLAN | No | Yes |
| Security | Port Security | Yes | Yes |
|  | Storm Control | Yes | Yes |
|  | DoS | Yes | Yes |
|  | Dynamic ARP Inspection | Yes | Yes |
|  | DHCP Snooping | Yes | Yes |
|  | IP Source Guard | Yes | Yes |
| ACL | MAC ACL | Yes | Yes |
|  | IPV4 ACL | Yes | Yes |
|  | IPV6 ACL | Yes | Yes |
| QoS | Port-based QoS | No | No |
|  | IEEE802.1p QoS | Yes | Yes |
|  | IP Precedence based CoS | Yes | Yes |
|  | DSCP based CoS | Yes | Yes |
|  | Priority Queues | 8 | 8 |
|  | Scheduling Algorithm | SP+WRR | SP+WRR |
| Rate Limiting | Ingress rate limiting | Yes | Yes |
|  | Egress rate limiting | Yes | Yes |
| Mirror | Port Mirroring on ingress and egress | Yes | Yes |
|  | Many to One | Yes | Yes |
| Log | System Log | Yes | Yes |
|  | Logging Server | No | Yes |
| Diagnostics | Ping | No | Yes |
|  | Traceroute | No | Yes |
|  | Cable Test | No | Yes |
|  | Fiber Module Information | No | Yes |
|  | UDLD | No | Yes |
| Management | User Account | Yes | Yes |
|  | WEB UI | Yes | Yes |
|  | CLI | No | Yes |
|  | Telnet | Yes | Yes |
|  | Firmware upgrade by WEB UI | Yes | Yes |
|  | Firmware upgrade by TFTP | Yes | Yes |
|  | Dual Image | No | Yes |
|  | config upload/download by WEB UI | Yes | Yes |
|  | SNMP V1/V2/V3 | Yes | Yes |
|  | SNMP Trap | Yes | Yes |
|  | RMON | Yes | Yes |
| Loop Detection/Prevention | Loop detection | No | No |
|  | Loop prevention | Yes | Yes |

## Mechanical Drawings

## Front Panel

4.1   EMI/Safety

| Item | Description | Remark |
| --- | --- | --- |
| Safety | LVD EN60950-1: 2011+A2: 2013 |  |
| EMC | FCC Part 15,Subpart B:ANSI C63.4-2014 | class A |
|  | CE EN55032: 2010+AC:2011 EN55024: 2010+A1:2015 |  |