11ac 750Mbps High Power Outdoor Wireless AP

Model: Air Mo750

Description:

Air Mo750is an Qualcomm Solution 11ac high power industrial use Outdoor wireless access point with the next generation 802.11ac Wi-Fi standard, combined 750Mbps Wi-Fi speed over 2.4GHz(300Mbps) and 5GHz(450Mbps), fast Ethernet data rate make100+ end users can access into it to enjoy seamless HD movies, streaming, online gaming, wireless security and other bandwidth-intensive tasks.

ABS waterproof, dust proof and sunscreen shell, temperature adaptive and board protective

Air Mo750with ABS waterproof, dust proof and sunscreen shell, avoid the damage from dust, rainy weather. Meantime, it adaptive to various environment, the working temperature can be normal at -40℃ to 55℃. Suit for any country.

High Power, 5dBi omni antenna, more WiFi Range

Designed in two line Power Amplifier on PCB board, the power can be 500mW high power, build in 3PCS omni antenna, outdoor WiFi range up to 500 meters.

Power over Ethernet

HW-AP750 has integrated Power over Ethernet (PoE), for easy installation and lower cost. So it can be installed in areas where power outlets are not readily available, eliminating the mess of altering existing network infrastructure. Pls note, the default is 24V Passive PoE; 48V IEEE 802.3af active PoE is optional by extra price.

Access Controller System & Cloud Management System

Work with WLAN controller in wireless AP operation mode,easily access advanced network settings through PC, like AP status monitor, change IP address, ESSID, Channel, Password, upgrade firmware, backup and restore....

Then work with Cloud Management System, easy to do central and remote management, advertisement and multi authentication make this device more professional in WiFi Projects.

Main Features:

- Comply with IEEE 802.11ac/b/g/n, dual band, 750Mbps Data Rate

- 1*10/100Mbps WAN Port，1*10/100Mbps LAN Port

- 500mW high power, Qualcomm Chipset, 16M Flash, 128M DDR2 RAM, more user, more stable

- Support 24V Passive PoE or 48V IEEE 802.3af POE

- Support SSID broadcasting, Multi SSID up to 8 (4 SSID in 2.4GHz, 4 SSID in 5GHz), support tag VLAN based on SSID to protect the whole data safety.

- Support Gateway (PPPOE, static IP, dynamic IP) , Wireless AP, Repeater, WISPoperation mode

- With function of firewall, IP filter, URL filter and MAC filter

- Comply with IEEE 802.3az standard,RF power adjustment and frequency analyzer for better application in different environment

- Support DDNS, VPN pass through, Port forwarding and DMZ host

- Support 64/128-bit WEP security, 128bit WPA (TKIP/AES) security

Product Spec.:

| Hardware: |
| --- |
| Chipset | Qualcomm QCA9531+QCA9887 |
| Standard | 802.11ac/b/g/n, MIMO technology |
| Memory | 128MB DDR2 RAM |
| Flash | 16MB |
| Interface | 1 * 10/100Mbps RJ45 WAN Port |
|  | 1 * 10/100Mbps RJ45 LAN Port |
|  | 1 * Reset button, press 15 seconds to revert to default setting |
| Antenna | 3PCS omni antenna, 5dBi |
| Power consumption | 24V PoE<10W； 48V IEEE802.3af POE <15W |
| Size | 315mm * 145 mm * 80 mm |
| RF Data |
| Frequency | 2.4G:802.11b/g/n; 5GHz: 802.11a/n/ac |
|  | 2.4GHz: 2.4~2.4835GHz, 5GHz: 5180~5825MHz |
| Country code | FCC、IC、ETSI、MKK、MKK1、MKK2、MKK3、NCC、RUSSIAN、CN |
| Modulation | OFDM = BPSK,QPSK, 16-QAM, 64-QAM |
|  | DSSS = DBPSK, DQPSK, CCK |
| Data Rate | 750 Mbps (2.4G 300Mbps, 5.8G 450Mbps) |
| Receive Sensitivity & RF Power |
| RF Power | 2.4G: 11n @MCS7:22±2DB, @MCS0:24±2DB. 11g @54M:23±2DB, @6M:25±2DB. 11b @11M:25±2DB, @1M:27±2DB. 5.8G: 11a @54M:22±2DB, @6M:24±2DB. 11n @MCS7:20±2DB, @MCS0:22±2DB. 11ac @MCS9:19±2DB, @MCS0:21±2DB. |
| Receive Sensitivity | 2.4G: 11n: -70dbm@MCS7, -88dbm@MCS0. 11g: -72dbm@54Mbps, -88dbm@6Mbps. 11b: -85dbm@11Mbps, -94dbm@1Mbps. 5.8G: 11a: -72dbm@54Mbps, -90dbm@6Mbps. 11n: -70dbm@MCS7, -90dbm@MCS0. 11ac:-60dbm@MCS9, -86dbm@MCS0. |
| EVM | 11n: ≤-28 DB 11g: ≤-25 DB 11b: ≤-10 DB 11a: ≤-25 DB |
| PPM | ±20ppm |
| Firmware Features: |
| Operation mode | Wireless AP, Gateway, WISP, WiFi Repeater |
| WAN Type | Dynamic IP/Static IP/PPPoE/L2TP(Dual Access) /PPTP(Dual Access) |
| Wireless Security | 64/128-bit WEP, WPA / WPA2, WPA-PSK/ WPA2-PSK, 802.1x encryption |
| SSID | Multiple SSID (4 SSID for 2.4G, 4 SSID for 5.8G) |
| Firewall | DoS, SPI Firewall, IP Address Filter/MAC Address Filter/Domain Filter IP and MAC Address Binding |
| Protocols | IPv4 |
| Others: |
| Package Contents | 750Mbps Dual Band wireless access point PoE Adapter Ethernet Cable Quick Installation Guide Setting Accessory |
| System Requirements | Microsoft Windows 98SE, NT, 2000, XP, Vista™ or Windows 7, Windows 8, MAC OS, NetWare, UNIX or Linux |
| Environment | Operating Temperature: -40~55 ℃, Storage Temperature: -40~70 ℃ Operating Humidity: 10%~90% non-condensing; Storage Humidity: 5%~90% non-condensing |
| Management | Firmware GUI , Remote Management, WLAN Controller, Cloud Management System |