## AP-SGX5500 Series 10G Uplink Security Switch

SGX5500 series are designed for class-carrier GE access and 10G uplink network; they cover all kinds of enterprise/ operators customer. It provides 20/24/48* 10/100/1000Base-T, 1000Base-X SFP or 10G SPF+ for the demand of cost-effective Gigabit access / aggregation. SGX5500 adopts high performance processor to provide full speed forwarding and line-dormant capacity to coordinate with NGGN unified software. It supports strong ACL and IP+MAC+ports binding etc.

| SGX5500-28TX |  |
| --- | --- |
|  | □24*10/100/1000Base-T □4*10GE SFP+ □ 12K Jumbo, 16K MAC, 4K VLAN □ 2K ACL,IP+MAC+Port+VLAN binding □ full load <40W □ WEB/SNMP/Telnet □AC：Input 90～260V，50～60Hz □440mm*220mm*44mm |
| SGX5500-52TX |  |
|  | □48*10/100/1000Base-T □4*10GE SFP+ □ 12K Jumbo, 16K MAC, 4K VLAN □ 2K ACL, IP+MAC+Port+VLAN binding □ full load<60W □ WEB/SNMP/Telnet □AC：Input 90～260V，50～60Hz □440mm*300mm*44mm |

| SGX5500-28SX |  |
| --- | --- |
|  | □20*100/1000Base-X, □4*GE Combo □4*10GE SFP+ □ 12K Jumbo, 16K MAC, 4K VLAN □ 2K ACL, IP+MAC+Port+VLAN binding □ full load<60W □ WEB/SNMP/Telnet □AC：Input 90～260V，50～60Hz □440mm*280mm*44mm |

Product Specifications:

| Item | SGX5500-28TX | SGX5500-52TX | SGX5500-28SX |
| --- | --- | --- | --- |
| Interface switching capacity | 128Gbps | 176Gbps | 128Gbps |
| Forwarding capacity | 95Mpps | 130Mpps | 95Mpps |
| Memory and flash | 512MB SDRAM memory and 16MB flash |
| Power | AC：Input 90～260V，50～60Hz； |
| Power consumption | Full-loaded≤40W Idle≤13W | Full-loaded≤60W Idle≤25W | Full-loaded≤60W Idle≤20W |
| Dimensions (width x depth x height)) | 440mm*220mm*44mm | 440mm*300mm*44mm | 440mm*280mm*44mm |
| Weight (Full-loaded) | ≤3.5kg | ≤3kg | ≤3kg |
| Environmental requirements | Working temperature：-15(C～55(C Storage temperature：-40(C～70(C Relative humidity：10%～90%，non-condensing |

- Business Features:

| Item | SGX5500-28TX/52TX/28SX |
| --- | --- |
| L2 features | MAC | 16K MAC address MAC Black Hole Port MAC Limit |
|  | VLAN | 4K VLAN entries Port based QinQ PVLAN to realize port isolation and saving public-vlan resources GVRP |
|  | Spanning tree | STP/RSTP/MSTP Remote-loop-detect |
|  | Port | Bidirectional bandwidth control, configure entry/exit and the smallest 64K control particle Static and LACP Port- mirroring of 1:1 or N:1 |
| Security features | User’s security | ARP anti-Flooding, configure ARP traffic safety threshold and inhibition ARP packet ARP anti-Spoofing, configure ARP inner and outer MAC check and static ARP checklist and drop / flood action IP+MAC+port+VLAN binding manually Port Isolation, configure hardware isolation of each port文 Bind MAC address to port and MAC address filtration on port IEEE 802.1x and AAA/Radius authentication |
|  | Device security | Anti-DOS attack SSHv2 Secure Shell SNMP v3 encryption Telnet based on Security IP Prevent unauthorized user |
|  | Network security | One button binding based on dynamic ARP table Manual binding parameter of IP 、VLAN ID、MAC and port etc. L2-L7 ACL flow filtration Auto-shutdown port in storm Update user’s location through DHCP Option82 and PPP |
| Service features | ACL | Activate standard and extended ACL Time Range ACL strategy Flow classification based on SMAC、DMAC、VLAN、SIP、DIP、IP IP(IPv4/IPv6) 、TCP/UDP port num、 protocol type etc. Packet filtration of L2～L7 IP header with 80bytes |
|  | QoS | Rate-limit to packet sending/receiving speed of port or self-defined flow and provide general flow monitor and two-speed tri-color monitor of self-defined flow Packet mirror and redirection of interface and self-defined flow Supports Priority remark to port or self-defined flow and provide 802.1P, DSCP priority and Remark Super queue scheduler based on port and self-defined flow. Each port/ flow supports 8 priority queues and scheduler of SP, WRR and SP+WRR |
|  | Multicast | IGMPv1/v2/v3 Snooping IGMP Filter MVR multicast VLAN register and cross VLAN multicast replication IGMP Fast leave IGMP Proxy |
| Reliability | Loop protection | EAPS and GERP Loopback-detection |
|  | Link protection | FlexLink RSTP/MSTP LACP |
|  | Device protection | Backup of host program and configuration files |
| Maintenance | Network maintenance | Port real-time, utilization and transmit/receive statistic based on CLI Port real-time, utilization and transmit/receive statistic based on CLI 802.3ah Ethernet OAM Syslog and RFC 3164 BSD syslog Protocol Ping and Traceroute |
|  | Device management | CLI, Console port, Telnet and WEB SNMPv1/v2/v3 RMON (Remote Monitoring)1,2,3,9 group MIB NTP GN.LinkⅡ Server NGBNView network management |

Purchase Information:

| Product name | Product description |
| --- | --- |
| SGX5500-28TX | 24*10/100/1000Base-T,4*10GE SFP+（100~240V AC;50/60Hz） |
| SGX5500-52TX | 48*10/100/1000Base-T,4*10GE SFP+ （100~240V AC;50/60Hz） |
| SGX5500-28SX | 20*100/1000Base-X, 4*GE Combo,4*10GE SFP+（100~240V AC;50/60Hz） |

# Text boxes

2600-18TC

2600-18TC

2600-18TC