300Mbps Wall Mount Wireless Access Point

Model: WAP100E

# Description:

# AirPro WAP100E is an in wall AP with Qualcomm chipset, providing Internet access at a data rate of 300Mbps. It is designed principally for Hotel to provide guests and roomers secure Internet access in their hotel room, guest room, living room and lobby.

# It supports 802.3af PoE, compliant with any 802.3af Power over Ethernet equipment, easy to install and provides complete Wi-Fi coverage.

# Managed by WLAN controller, easy to configure data centrally or remotely; also it works with cloud server for portal authentication and advertisement function.

# Key Features:

- In Wall Panel Design
Matches with cassette size of 86mm or 75mm, effortlessly provide Wi-Fi and matches with design style.

- Wireless N and 300Mbps Speed 
Compliant with IEEE 802.11b/g/n standard; comes with a data rate of 300Mbps providing the seamless Internet surf and faster downloads.

- Power over Ethernet 
It supports 802.3af PoE, can be powered by any 802.3af Power over Ethernet equipment, making it a cost-effective solution.

- Multi SSID and LAN Port Tag VLAN
PW520 supports 4 SSID; each SSID can be tagged for a specified network VLAN for different user access, based on established access rights and Internet safety.

- Centralized Management and Portal Authentication 
It supports WLAN controller for centralized management, allowing IT staff to set up separate IP addresses, ESSID and manages AP's of each room at the same time. Also, they can remotely add, set up, monitor, delete and upgrade firmware via the WLAN controller through computer.

In addition, it works with the cloud server for remote management, then with function of accounting, Facebook / Google authentication, SMS verification and so on.

# Specifications

| Wireless |
| --- |
| Standards | IEEE 802.11n, IEEE 802.11g, IEEE 802.11b |
| Data Rate | 11n: 300Mbps 11g: 54Mbps 11b: 11Mbps |
| Frequency Range | 2.4-2.4835GHz |
| Wireless Transmit Power | 11n @MCS7:14±2DB, @MCS0:16±2DB. 11g @54M:15±2DB, @6M:17±2DB. 11b @11M:18±2DB, @1M:20±2DB. |
| Modulation Type | OFDM = BPSK,QPSK,16-QAM,64-QAM;DSSS = DBPSK,DQPSK,CCK |
| Receive Sensitivity | 11n: -70dbm@MCS7, -88dbm@MCS0. 11g: -72dbm@54Mbps, -88dbm@6Mbps. 11b: -85dbm@11Mbps, -94dbm@1Mbps. |
| EVM | 802.11n: ≤-28 DB 802.11g: ≤-25 DB 802.11b: ≤-10 DB |
| PPM | ±20ppm |
| MAX Users | 64 |
| Operation Mode | Gateway, AP, Repeater |
| Wireless Security | 64/128-bit WEP, WPA/WPA2, WPA /WPA2-Personal (TKIP/AES) |
| System Requirements | Windows 7/Vista/XP/2000,Mac OS®, Linux or Android OS |
| Hardware |
| Chipset | Atheros QCA9531 |
| Flash | 16M |
| SDRAM | 64M |
| Interfaces | 2 x 10/100Mbps LAN/WAN Port |
| Button | Reset Button |
| Antenna | MIMO 3dBi Build-in omni-directional Antenna |
| Power Supply | 802.3af PoE |
| Dimensions( W x D x H ) | 86*86*68mm |
| Others |
| Operating Temperature | -20°C~55°C |
| Storage Temperature | -40°C~70°C |
| Relative Humidity | 10% ~ 90%, Non-condensing |
| Storage Humidity | 5%~95%, Non-condensing |
| Certifications | RoHS |
| Package Contents | 1 x in wall AP 1 x Quick Installation Guide 1 x setting accessory |