750Mbps Dual Band Wall Mount Wireless AP

Model:  WAP2750E

Description:

AirPro WAP2750E is an SNMP protocol based 11ac Wall Mount style Wireless Access Point. Upgrade to the latest wireless-AC technology and enjoy the seamless internet at fast data rates (433Mbps in 5G and 300Mbps in 2.4GHz), dual band allows seamless stream, faster content download and quickly sync large video or music files. It comes embedded with PoE, providing a steady wireless network in Hotel, School and Hospital. Additionally, it works with AirPro Access Controller system and cloud management system providing easy central configuration, meet with different advertisement and multi authentication requirements, which makes it a professional and cost effective solution for large area Wi-Fi.

Wireless AC Technology, More Users

The WAP2750E is a dual band wall mount Wireless Access Point offering wireless-AC technology for seamless/smoother video and music streaming, with this technology several users can share data over the Wi-Fi networks and can even watch online Internet-ready TV, play games and other Wi-Fi devices can access into this wireless networking at transfer rates of up to 750Mbps speed.

Dual Band, Less Interference

Double your network bandwidth with this Dual-Band AC (2.4G and 5G) which is designed to avoid interference and maximize throughput. You can browse web pages, handle mails and chat over 2.4G, while enjoying lag-free HD multimedia and online gaming over 5G without worrying about any interference.

Power over Ethernet

WAP2750E AC AP has integrated with IEEE 802.3af standard Power over Ethernet (PoE), for easy installation and is available at affordable cost. Therefore, it can be installed in areas where power outlets are not promptly accessible, thereby eliminating the mess of altering existing network infrastructure.

Access Controller System & Cloud Management System

WAP2750E works with Access Control System, allows easy access to advanced network settings through PC, including AP status monitor, change IP address, ESSID, channel, password, upgrade firmware, backup and restore, etc.

Additionally, it works with Cloud Management System, providing easy central and remote management, advertisement and multi authentication. Also, the billing function is likely to be included in the near future, which makes this AP more professional in Wi-Fi Projects.

Main Features:

Compatible with 802.11ac wireless technology, work with 802.11ac/b/g/n device

1 * 10/100Mbps WAN port, 1 * 10/100Mbps LAN port, WAN port support IEEE 802.3af  PoE.

Simultaneous Dual-Band with speeds up to 750Mbps at 2.4GHz and 5GHz band concurrently

16M Flash + 128M DDRII RAM, more stable performance in wireless

Easy setup, remote and central managed by access controller system and Cloud management system

SPEC:

| HARDWARE FEATURES |
| --- |
| Interface | 1 * 10/100Mbps WAN Port 1 * 10/100Mbps LAN Port 1 * LED on/off switch |
| Button | Reset Button, press 15 seconds to revert to default data. |
| Chipset | Qualcomm QCA9531+QCA9887 |
| Flash | 16M Flash |
| SDRAM | 128M DDR |
| External Power Supply | 48V PoE, IEEE 802.3af standard |
| Dimensions (W X D X H) | 86*86*35mm |
| Antenna Type | 1*5.8GHz 2dBi internal antenna 2 * 2.4GHz 2dBi internal antennas |

| WIRELESS FEATURES |
| --- |
| Wireless Standards | IEEE 802.11ac/n/a 5GHz; IEEE 802.11n/g/b 2.4GHz |
| Frequency | 5GHz and 2.4GHz |
| Signal Rate | 5GHz:Up to 433Mbps; 2.4GHz: Up to 300Mbps |
| EIRP | <20dBm(EIRP) |
| Reception Sensitivity | 2.4G: 11n: -70dbm@MCS7, -88dbm@MCS0. 11g: -72dbm@54Mbps, -88dbm@6Mbps. 11b: -85dbm@11Mbps, -94dbm@1Mbps. 5.8G: 11a: -72dbm@54Mbps, -90dbm@6Mbps. 11n: -70dbm@MCS7, -90dbm@MCS0. 11ac:-60dbm@MCS9, -86dbm@MCS0. |
| RF Power | 2.4G: 11n @MCS7:15±2DB, @MCS0:17±2DB. 11g @54M:16±2DB, @6M:18±2DB. 11b @11M:18±2DB, @1M:20±2DB. 5.8G: 11a @54M:15±2DB, @6M:17±2DB. 11n @MCS7:14±2DB, @MCS0:16±2DB. 11ac @MCS9:13±2DB, @MCS0:15±2DB. |
| Wireless | Auto-Channel selection |
|  | Distance Control (802.1x Ack timeout) |
|  | Multiple SSID (4 SSID for 2.4G, 4 SSID for 5.8G) |
|  | BSSID |
| EVM | 802.11n: ≤-28 DB 802.11g: ≤-25 DB 802.11b: ≤-10 DB 802.11a: ≤-25 DB |
| PPM | ±20ppm |
| Max Access Users | 128 |
| Operation Mode | Wireless AP, Gateway, WiFi Repeater |
| Wireless Security | 64/128-bit WEP, WPA / WPA2, WPA-PSK/ WPA2-PSK encryption |
| LED Status | Sys(System), WAN, WiFi |
| Management |
| System Settings | Web-based configuration (HTTP/Telnet), Access Control System (SNMP) |
| Firmware Upgrade | Upgrade firmware via web browser or TFTP |
| Administration | Admin Password can be configured |
| System monitoring | Watch dog, Status in hand , useful statistic and Event log |
| Logs | Supports local logs, logs host, logs file export |
| Reset | Reset or factory defaults |
| Backup | Restore settings & configuration of the device to local file, Scheduled reboot |

| OTHERS |
| --- |
| Certification |  |
| Package Contents | 750Mbps Dual Band wireless access point Ethernet Cable Quick Installation Guide Setting Accessory |
| System Requirements | Microsoft Windows 98SE, NT, 2000, XP, Vista™ or Windows 7, Windows 8, Windows 10, MAC OS, NetWare, UNIX or Linux |
| Environment | Operating Temperature: -40~55 ℃ Storage Temperature: -40~70 ℃ Humidity: 5%~95% non-condensing |